o Service menu 1: VOLT:55 :45

The first value is the current voltage value. The second one is the voltage value corresponding for the “Empty battery” status. Pressing “Ok” will store the current value. This is bad, since your current value is usually greater than default value and after that your transceiver will report “Empty battery” on the current value. If accidentally “Ok” pressed, you will need a variable external power source. Just plug in the jack and careful vary the voltage until the current value is 45. Press “Ok” and all is fine;-)

My transceiver is working from about 4.7V. However, on this voltage, the transmit power is lower and, on max volume, the audio will start “howling”. From 5.4V the audio is fine, the battery is not charged and the transceiver remain cold.

o Service menu 2: TCXO: 40 :40

o Service menu 3: BPF:** f1:**:

Band depending values. A default value for each band follows:

b1-> BPF:24 f1:24

b2-> BPF:03 f1:03

b3-> BPF:22 f1:22

b4-> BPF:22 f1:22

b5-> BPF:18 f1:18

b6-> BPF:18 f1:18

b7-> BPF:18 f1:18

b8-> BPF:18 f1:18

b9-> BPF:** f1:**

b10-> BPF:** f1:**

b11-> BPF:** f1:**

o Service menu 4: BPF:** f2:**:

Band depending values. A default value for each band follows:

b1-> BPF:59 f2:59

b2-> BPF:61 f2:61

b3-> BPF:71 f2:71

b4-> BPF:71 f2:71

b5-> BPF:44 f2:44

b6-> BPF:44 f2:44

b7-> BPF:44 f2:44

b8-> BPF:44 f2:44

b9-> BPF:** f2:**

b10-> BPF:** f2:**

b11-> BPF:** f2:**

o Service menu 5: BPF:** f3:**:

Band depending values. A default value for each band follows:

b1-> BPF:C2 f3:C2

b2-> BPF:BC f3:BC

b3-> BPF:9D f3:9D

b4-> BPF:9D f3:9D

b5-> BPF:77 f3:77

b6-> BPF:77 f3:77

b7-> BPF:77 f3:77

b8-> BPF:77 f3:77

b9-> BPF:** f3:**

b10-> BPF:** f3:**

b11-> BPF:** f3:**

o Service menu 6: 2nd:39-25:39

o Service menu 7: 2nd:8b 0:8b

o Service menu 8: 2nd:e8+25:e8

o Service menu 9: BFO:72 CW:FF

o Service menu 10: BFO:9B LS:9B

o Service menu 11: BFO:09 US:09

o Service menu 12: SQ:varies 34-37 1:27

The first value varies and is band depending. A default value for each band follows:

b1-> SQ: varies 54-57 1:FF

b2-> SQ: varies 54-57 1:1F

b3-> SQ: varies 54-57 1:27

b4-> SQ: varies 54-57 1:FF

b5-> SQ: varies 54-57 1:1B

b6-> SQ: varies 54-57 1:23

b7-> SQ: varies 54-57 1:FF

b8-> SQ: varies 54-57 1:2C

b9-> SQ: varies 54-57 1:27

b10-> SQ: varies 54-57 1:FF

b11-> SQ: varies 54-57 1:2D

o Service menu 13: SQ varies 34-35 2:20

The first value varies and is band depending. A default value for each band follows:

b1-> SQ: varies 53-53 2:FF

b2-> SQ: varies 34-35 2:1A

b3-> SQ: varies 34-35 2:20

b4-> SQ: varies 34-35 2:FF

b5-> SQ: varies 34-35 2:18

b6-> SQ: varies 34-35 2:1C

b7-> SQ: varies 34-35 2:FF

b8-> SQ: varies 34-35 2:24

b9-> SQ: varies 34-35 2:20

b10-> SQ: varies 34-35 2:FF

b11-> SQ: varies 34-35 2:25

o Service menu 14: SM:varies 37-38 S1:5A

The first value varies and is band depending. A default value for each band follows:

b1-> SM: varies 42-43 S1:69

b2-> SM: varies 37 S1:64

b3-> SM: varies 37 S1:5B

b4-> SM: varies 37 S1:1B

b5-> SM: varies 37 S1:6F

b6-> SM: varies 37 S1:64

b7-> SM: varies 37 S1:1A

b8-> SM: varies 37 S1:4A

b9-> SM: varies 37 S1:5A

b10-> SM: varies 37 S1:1A

b11-> SM: varies 37 S1:46

o Service menu 15: SM: varies 37-38 S9:81

The first value varies and is band depending. A default value for each band follows:

b1-> SM: varies 37-38 S9:92

b2-> SM: varies 37-38 S9:89

b3-> SM: varies 37-38 S9:82

b4-> SM: varies 37-38 S9:6D

b5-> SM: varies 37-38 S9:87

b6-> SM: varies 37-38 S9:82

b7-> SM: varies 37-38 S9:62

b8-> SM: varies 37-38 S9:6B

b9-> SM: varies 37-38 S9:81

b10-> SM: varies 37-38 S9:50

b11-> SM: varies 37-38 S9:6E

o Service menu 16: P:** BAf1:**

Band depending value. For Rx only bands, the values are **. A default value for each Tx band follows:

b6-> P:14 BAf1:14

b8-> P:18 BAf1:18

b9-> P:19 BAf1:19

o Service menu 17: P:** Baf2:**

Band depending value. For Rx only bands, the values are **. A default value for each Tx band follows:

b6-> P:14 BAf2:14

b8-> P:18 BAf2:18

b9-> P:19 BAf2:19

o Service menu 18: P:** Baf3:**

Band depending value. For Rx only bands, the values are **. A default value for each Tx band follows:

b6-> P:14 Baf3:14

b8-> P:18 Baf3:18

b9-> P:19 Baf3:19

o Service menu 19: P:** 7f1:**

Band depending value. For Rx only bands, the values are **. A default value for each Tx band follows:

b6-> P:14 7f1:14

b8-> P:18 7f1:18

b9-> P:19 7f1:19

o Service menu 20: P:** 7f2:**

Band depending value. For Rx only bands, the values are **. A default value for each Tx band follows:

b6-> P:14 7f2:14

b8-> P:18 7f2:18

b9-> P:19 7f2:19

o Service menu 21: P:** 7f3:**

Band depending value. For Rx only bands, the values are **. A default value for each Tx band follows:

b6-> P:14 7f3:14

b8-> P:18 7f3:18

b9-> P:19 7f3:19

o Service menu 22: P:** 13f1:**

Band depending value. For Rx only bands, the values are **. A default value for each Tx band follows:

b6-> P:24 13f1:24

b8-> P:29 13f1:29

b9-> P:2C 13f1:2C

o Service menu 23: P:** 13f2:**

Band depending value. For Rx only bands, the values are **. A default value for each Tx band follows:

b6-> P:24 13f2:24

b8-> P:29 13f2:29

b9-> P:2C 13f2:2C

o Service menu 24: P:** 13f3:**

Band depending value. For Rx only bands, the values are **. A default value for each Tx band follows:

b6-> P:24 13f3:24

b8-> P:29 13f3:29

b9-> P:2C 13f3:2C

o Service menu 25: BAL:** f1:**

Band depending value. For Rx only bands, the values are **. A default value for each Tx band follows:

b6-> BAL:40 f1:40

b8-> BAL:33 f1:33

b9-> BAL:32 f1:32

o Service menu 26: BAL:** f2:**

Band depending value. For Rx only bands, the values are **. A default value for each Tx band follows:

b6-> BAL:3F f2:3F

b8-> BAL:33 f2:33

b9-> BAL:32 f2:32

o Service menu 27: BAL:** f3:**

Band depending value. For Rx only bands, the values are **. A default value for each Tx band follows:

b6-> BAL:3E f3:3E

b8-> BAL:33 f3:33

b9-> BAL:33 f3:33

o Service menu 28: MAX:** f1:**

Deviation level. For bigger modulation, increase this value. Band depending value. For Rx only bands, the values are **. A default value for each Tx band follows:

b6-> MAX:7C f1:7C

b8-> MAX:3D f1:3D

b9-> MAX:1D f1:1D

o Service menu 29: MAX:** f2:**

Band depending value. For Rx only bands, the values are **. A default value for each Tx band follows:

b6-> MAX:7A f2:7A

b8-> MAX:3D f2:3D

b9-> MAX:2D f2:2D

o Service menu 30: MAX:** f3:**

Band depending value. For Rx only bands, the values are **. A default value for each Tx band follows:

b6-> MAX:7B f3:7B

b8-> MAX:3D f3:3D

b9-> MAX:2E f3:2E

o Service menu 31: TON:** f1:**

Band depending value. For Rx only bands, the values are **. A default value for each Tx band follows:

b6-> TON:96 f1:96

b8-> TON:63 f1:63

b9-> TON:30 f1:30

o Service menu 32: TON:** f2:**

Band depending value. For Rx only bands, the values are **. A default value for each Tx band follows:

b6-> TON:98 f2:98

b8-> TON:63 f2:63

b9-> TON:30 f2:30

o Service menu 33: TON:** f3:**

Band depending value. For Rx only bands, the values are **. A default value for each Tx band follows:

b6-> TON:95 f3:95

b8-> TON:63 f3:63

b9-> TON:2F f3:2F

o Service menu 34: DCS:** f1:**

Band depending value. For Rx only bands, the values are **. A default value for each Tx band follows:

b6-> DCS:6A f1:6A

b8-> DCS:45 f1:45

b9-> DCS:23 f1:23

o Service menu 35: DCS:** f2:**

Band depending value. For Rx only bands, the values are **. A default value for each Tx band follows:

b6-> DCS:6A f2:6A

b8-> DCS:45 f2:45

b9-> DCS:23 f2:23

o Service menu 36: DCS:** f3:**

Band depending value. For Rx only bands, the values are **. A default value for each Tx band follows:

b6-> DCS:6B f3:6B

b8-> DCS:45 f3:45

b9-> DCS:22 f3:22

o Service menu 37: 96:** f1:**

Band depending value. For Rx only bands, the values are **. A default value for each Tx band follows:

b6-> 96:7A f1:7A

b8-> 96:53 f1:53

b9-> 96:2A f1:2A

o Service menu 38: 96:** f2:**

Band depending value. For Rx only bands, the values are **. A default value for each Tx band follows:

b6-> 96:78 f2:78

b8-> 96:53 f2:53

b9-> 96:2B f2:2B

o Service menu 39: 96:** f3:**

Band depending value. For Rx only bands, the values are **. A default value for each Tx band follows:

b6-> 96:7B f3:7B

b8-> 96:53 f3:53

b9-> 96:2A f3:2A

o Service menu 40: VOX:00 1:46

o Service menu 41: VOX:00 9:1A